|  | KJF501 |
| --- | --- |
| Chemical Air filter is designed for solving the problem of corrosion and odor contamination (VOCs, SO2, NO2, H2O, Ammonia, NMP, HCl, HF, H2SO4, Ozone) in industrial environment. There are four (4) types of Air Filters available which offer some level of AMC removal: Carbon Slurry Coated Type Carbon Tray Type Honey-Comb Type Carbon Loaded Web in Pleated Form | Carbon Slurry Coated Type Activated Carbon Filter 植入式浪型活性碳濾網 Performance Parameter 執行變數 Carbon Slurry Coated Type Activated Carbon Filter植入性濾網 Tray Type Activated Carbon Filter填充式濾網 Honey-Comb Type Activated Carbon Filter 蜂巢式濾網 Carbon Loaded Web Type Activated Carbon Filter包覆式濾網 Low Pressure Drop 低壓損 + + or - + or - + Weight of Activated Carbon 活性碳重量 - ++ ++ +++ Optimal Activated Carbon Size 最理想的活性碳尺寸 + - + ++++ Overall Adsorption Efficiency 整體吸附效率 --- + + +++ Low Dust 低灰塵 + -- - ++ Pleated Ability 壓褶能力 + N/A N/A ++++ Easy of Replacement 更換簡易 + -- + + Features: Carbon slurry coated type (Polysorb Activated Carbon Media): are typically coated power carbon with adhesive into foam woven. Activated carbon can effectively remove chemicals from air. Foam Woven design can also effectively reduce air speed and pressure drop, ensure maximum contact area with the filter and capacity. |

KJF501

Media: Implant the small size porous absorbent into the foam material, through irregular channels, let the air flow has more opportunity to increase contact with the adsorbent. The more wave forms, the more the wind speed can be slowed down through the filter and reduce the pressure drop, and increase the filter surface area and capacity. Filter’s outlet size using the filter support network (Support Grid), filter and iron mesh are 100% fitted to protect the media. The expanded metal mesh has better corrosion resistance than other metal mesh. Frame: The frame is available for Paper Frame and Metal Frame (Galvanized Steel, Aluminum and Stainless Steel). 特色：波浪式可減緩通過濾網的風速以降低壓損，並增加濾材的表面積及容量。可初步處理有機揮發物，去 除異味，更換方式簡便，成本也較低廉。 濾材：是將粒徑小的吸附劑植入多孔性的發泡材中，藉由不規則的孔道讓氣流通過時增加與吸附劑接觸的機會；為了要減低穿過濾網氣流的風速將濾網作波浪式，摺數愈多或愈深，愈可減緩通過濾網的風速降低壓損，並增加濾材的表面積及容量。濾材的出風面使用濾材支撐網，濾材100%和鐵網貼合，以保護濾材，被覆處理之擴張金屬網抗蝕性優於其他鐵網。 外框: 框材可選用紙框、鍍鋅鐵框、鋁框或不銹鋼框。

KJF501

Activated Carbon Filter Performance Data - Carbon Slurry Coated Type 活性碳濾網性能表 - 植入式浪型活性碳濾網 Nominal Size Actual Size Rated Capacity Initial Resistance Remove Efficiency 通稱尺寸 實際尺寸 額定風量 初壓損 去除效率 （W*H*D） （W*H*D） （inch） （mm） （CMH） (Pa) （％） 12*24*2 289*595*45 1700 65 Depending on field condition 依現場條件而定 20*20*2 492*492*45 2380 20*24*2 492*595*45 2800 24*24*2 595*595*45 3400 12*24*4 289*595*95 1700 45 20*20*4 492*492*95 2380 20*24*4 492*595*95 2800 24*24*4 595*595*95 3400 *Special Sizes are available upon request. ※特殊規格可生產製造。

KJF501

Material and Service Conditions 材質和使用條件 Type 型式 Description 說明 Construction 總成 Media 濾材 Non-Woven + Activated Carbon 不織布棉+活性碳粒 Frame Material 外框材質 Paper Frame 紙框 Metal Frame 金屬框 Support Grid 支撐網 Anticorrosion Metal Support Grid w/Radial Wedge Pleats 抗蝕性的金屬支撐網，採楔行結構 名 稱:康智富科技有限公司 統 編:29168436 地 址:新北市永和區仁愛路141巷30弄26號1樓 電 話:+886-2-29256286 傳 真:+886-2-29256096 E-MAIL :ks.best@msa.hinet.net